## Slide 1
C. Cuvelier and P. Thunis
JRC, European Commission
Ispra - Italy
Harmonisation in AQ Modelling
< CityDelta, EuroDelta, … Fairmode >
Fairmode, Cavtat, 10 Oct 2008

## Slide 2: Overview
Harmonisation, support to AQ policy
CityDelta project
  Objectives, Methodology
EuroDelta project
  Objectives, Methodology

## Slide 3: Need for Harmonisation
Need for Evaluation of the uncertainty in AQ modelling used for AQ policy (see Directive AAQ).
Is there a (consistent) difference between the fine scale (FS, 5km) and the large scale (LS, 50km) models?
Do AQ models produce consistent responses to emission-reduction policy scenarios;
What are the ranges of these responses ?
What is the robustness of AQ modelling
results in the policy context?

## Slide 4: Harmonisation as we see it
Analysis of individual Modelling results (Validation against Obs)
Intercomparison of Modelling results
Ensemble approach (mean/median of the Models)
Analysis of the variability around the Ensemble
Validation of the Ensemble model
Spin-off: improvement and further development of models
The Ensemble model is a useful tool in the frame of the Harmonisation of the individual model results.
It is often more robust and looks therefore more appropriate for policy purpose


## Slide 5: CityDelta

## Slide 6
Policy context: Clean Air For Europe (CAFE)
Launched in 2001 by the European Commission, CAFE was a programme of technical analysis aiming at the development of a long-term, integrated policy advice to protect against negative effects of air pollution on human health and the environment.
Resulting in the Thematic Strategy published Sept 05
Question: Which measures will lead to a cost-effective reduction of air-pollution health-related problems in European Cities? In particular for O3 and PM
CityDelta Objective:
How to include sub-grid effects into a Europe-wide health impact assessment for PM/Ozone?

## Slide 7
The JRC has coordinated:
A model inter-comparison exercise for urban-regional scale dispersion models focusing on 8 European cities to identify:
  the systematic differences (delta’s) between rural and urban background AQ (“Scale”),
  how these delta’s depend on emissions (“Emissions”),
  how these delta’s vary across cities (“Cities”),
  how these delta’s vary across models (“Models”)
  how these delta’s vary for PM and O3 (“Pollutants”).

## Slide 8
Driving force: WHO Review of health impact from air pollution
Damage from long-term exposure to PM2.5/PM10
  Not yet possible to distinguish potency of individual PM components
  No threshold value for health impact can be identified
  The levels of long-term mean concentrations are more important than (episodic) peak concentrations
  CityDelta - Indicator: Annual mean PM2.5/PM10 (W/S)
New evidence for mortality effects from ozone
  No firm evidence for no-effect level; but larger uncertainties for effects at low concentrations
  Thus also low ozone days are relevan
   CityDelta - Indicator: SOMO35 (*)
(*) Sum of exceedances over 35 ppb of the maximum of the daily 8-hour mean
O3 concentrations, calculated over the entire year

## Slide 9
Model | # of levels | Level | Domain | Resolution
CALGRID | 11 | 10m | CITYDELTA | 5-10
CAMx | 11 | 10m | CITYDELTA | 5-10
CHIMERE local | 6: surface-700hPa | SL (50m) | CITYDELTA | 5
CHIMERE regional | 6: surface-700hPa | SL (50m) | Europe | 50
EMEP Unified Model | 20: surface-100hPa | 1m | EMEP | 50
EMEP-v.1 | 20: surface-100hPa | 45m | EMEP | 50
EPISODE | 6: 25-2500m | 2m | CITYDELTA | 10
EUROS | 4 | 25m | CITYDELTA | 10-50
LOTOS local | 3: 0-3500m | ML | CITYDELTA | 5-10
LOTOS régional | 3: 0-3500m | ML | Europe | 50
MOCAGE | 47: surface-5hPa | 1st level (0-50m) | Paris, Milano | 10-50
MUSCAT | 22: 0-4400m | 1st level (0-33m) | CITYDELTA | 10
MUSE | 5 | 10m | CITYDELTA | 10
OFIS | 2 | ML | CITYDELTA | 5
REM3 local | 4: 0-3000m | SL | CITYDELTA | 5
REM3 regional | 4: 0-3000m | SL | Europe | 50
STEM-FCM | 11 | 10m | CITYDELTA | 5
TRANSCHIM | 10 | 50m | CITYDELTA | 5-10
15 Modelling teams: 7 regional-scale
11 urban-scale

## Slide 10
8 Cities:
London
Paris
Prague
Berlin
Copenhagen
Katowice
Milan
Marseille

## Slide 11
8 Emission Scenarios
0 --- 1999
1 --- 2010 CLE: Current Legislation
2 --- 2010 NOx MFR: Maximum Feasible Reduction
3 --- 2010 NOx (CLE+MFR)/2
4 --- 2010 VOC MFR
5 --- 2010 NOX and VOC MFR
6 --- 2010 PMcoarse MFR
7 --- 2010 PM2.5 MFR
NOx | CLE-1999 | MFR-1999
Prague | -34% | -62%
Milan | -36% | -53%
Paris | -42% | -65%
Berlin | -38% | -50%
Meteo: 1999 provided by Meteo-France (Aladin 10 km) or calculated.
Boundary conditions: provided by EMEP or calculated.
Long term simulations: full year for PM, 6 months for O3
Outputs delivered with resolution of 5-10 or 50 km

## Slide 12
Emission Inventories: Local vs Regional
NOx, CO, SOx estimates seems quite robust
PM estimates show 40-50% differences.
CityDelta has also contributed to a considerable
revision of the regional-scale (EMEP) emission data

## Slide 13
Model Validation: - The “Taylor” plots
        - The “Ensemble” model
CRMSE
Corr.
K.E.Taylor, 2001, JGR, 106, 7183-7192
O3
Bias
RMSE

## Slide 14
O3 Summer Mean
Fine scale Ensemble
Large scale Ensemble
BER MIL LON KAT PRA PAR
PM10 Winter
BER MIL PRA PAR
“Delta” Interpretation (City-Model)

## Slide 15
“Delta” Interpretation (Emission-Scale)
NOx Reduction
VOC Reduction
CLE-2000
SOMO35:
(CityDomain)
Fine scale Ensemble
Large scale Ensemble

## Slide 16
CLE-2000
NOx Reduction
VOC Reduction
“Delta” Interpretation (Emission-Scale)
Fine scale Ensemble
Large scale Ensemble
PM10:
(CityDomain)

## Slide 17: Discussion
A first approach for addressing urban air quality for Europe-wide health impact assessment has been developed and implemented – based on observations and City-Delta results
Urgent need for validation of the FR with monitoring data, hampered by lack of PM2.5 sites.
Presently, grid average wind speeds used. No consideration of topography. City-specific wind speeds should improve.
Which emission/population density is representative of a city (how to draw city borders)? This determines directly the size of the urban increment.

## Slide 18: Publications: Overview: Cuvelier,Thunis, Vautard, et al. Validation: Vautard, Thunis, Cuvelier, Builtjes, et al. Delta’s: Thunis, Rouïl, Cuvelier, et al. Emissions: Maffeis, et al. All: Atmos. Env.

## Slide 19: EuroDelta

## Slide 20
Project to evaluate uncertainty in SRRs used in AQ policy
  5 regional models: EMEP, MATCH, REM3, CHIMERE, LOTOS
  28 emission scenarios (2000, 2010, 2020) with area specific reductions (FR, GE, IT, NorthSea, MedSea)
  60 sectoral emission reductions (2010, 2020) in FR, SP,
  GE, UK, and MedSea
  Zoom studies for Marseille, and Athens (50km => 10 km)
  Use of the ENSEMBLE approach
  Objectives : - Source-receptor variability
- Spatial variability
- Meteorological variability
- Confidence limits for policy purposes

## Slide 21: Mean Ozone
BaseCase: Emissions 2000, Meteo 1999
  Differences between model results of about 10 ppb in the rural areas and over the countries ; largest differences in winter
  Model variabiliy of 10 ppb represents about 40% of the ensemble value
  Models are closer in highly populated areas and more different in rural areas and over the seas
max
ensemble
min
Countries
Notes: I would add a picture with the mean Ozone results for 2000 given by the ensemble – and keep the model variability picture
PR clarify reference year

## Slide 22: Main Publications: Validation: in Atm. Env. Delta’s: Report EuroDelta I (to appear) Report EuroDelta II (Sep 2008)

## Slide 23
http://aqm.jrc.it/eurodelta
Report + DVD available with Results
http://aqm.jrc.it/citydelta
DVD available with Results

## Slide 24: Need for Harmonisation
Need for Evaluation of the uncertainty in AQ modelling used for AQ policy.
Do AQ models produce consistent responses to emission-reduction policy scenarios;
What are the ranges of these responses ?
What is the robustness of AQ modelling
results in the policy context?

## Slide 25: Harmonisation as we see it (and as Fairmode may see it)
Analysis of individual Modelling results (Validation against Obs)
Intercomparison of Modelling results
Ensemble approach (mean/median of the Models)
Analysis of the variability around the Ensemble
Validation of the Ensemble model
Spin-off: improvement and further development of models
The Ensemble model is a useful tool in the frame of the Harmonisation of the individual model results.
It is often more robust and looks therefore more appropriate for policy purpose


## Slide 26: The JRC Evaluation-Visualisation Tool

## Slide 27
OBSERVATIONS
(surface, profiles,
plane, lidar…
MODEL 1
MODEL 2
MODEL 3, …
4-D Fields: Meteo, Chemistry, Aerosols
Pre-processing (Window Interface)
ASCII-BIN  CDF
MONIT
Observation Overview
SHOWALL
4D model data analysis
XZ, YZ, SZ, XY Sections
Comparison with obs.
VALID
Statistical Module
Multi-models
(obs .vs. models)

## Slide 28
MONIT
Station Overview
Station raw data

## Slide 29
SHOWALL

## Slide 30
VALID